## Slide 1: Networking 101, Day 2 Ports, Protocols, and the OSI Model

## Slide 2: Class Objectives
By the end of today’s class, you will be able to:
Associate common protocols with their assigned ports.
Interpret data in network packets by analyzing their headers, payloads, and trailers.
Explain the role of ports in specifying a network packet's destination.
Explain how encapsulation and decapsulation allow different protocols to interact with one another.
Use the layers of the OSI model to identify the source of problems on a network.
Capture and analyze live network traffic using Wireshark.
2

## Slide 3: Protocols “Roger, Over, and Out”
3

## Slide 4
4
With so much going on behind-the-scenes in network communication, it’s important to have systems in place to avoid the many potential errors.
Notes: Image source: Matthew Butler

## Slide 5: Real World Protocols
When military personnel need to exchange messages over a radio, they may encounter the following issues:
Communications don't come in clearly.
Multiple communications are sent at the same time.
Communications are cut off.
5
Notes: Image source: shutterstock_778697080

## Slide 6: Real World Protocols 1 2
Military personnel use communication protocols to ensure messages
are transmitted, received, and understood clearly.
6
“Are you there? Over.”
“Roger, I am here, over.”
“Start the attack at noon, over.”
“Roger, out”.
Notes: Image source: shutterstock_778697080

## Slide 7: Real World Protocols
This mode of communication ensures that there is no ambiguity when sending and receiving messages. Clear meanings for certain keywords and strict rules for using them drastically improves the efficacy of communications.
7
“Over” signals the end of a specific line of communication.
“Roger” signals that the message was received completely.
“Out” signals that the message was received, the exchange is complete, and the order will be followed.
7
Notes: Image source: shutterstock_616290890

## Slide 8: These strict rules are known as a protocol. They impose structure by specifying the precise meaning of keywords, and where in a message they must appear.
8

## Slide 9: Protocols and Networks
9
Networks use protocols to ensure messages are fully sent and understood.
Similar to the military’s use of “over,” a network uses the TCP message FIN to indicate the end of the transmission.
Notes: Image source: Jake Kemper

## Slide 10: Networking Protocols
Some common protocols you may be familiar with:
The FTP protocol is used to transfer over a file.
10
FTP is used to transfer files.
HTTP is used to communicate web traffic.

## Slide 11: Networking Protocols
PAP is used for authenticating a user.
SMB is a Windows-based protocol for sharing files.
NetBIOS allows computers to communicate on a local network.
Some other important protocols:
11

## Slide 12
12
As we know from the previous class, the client and server communicate by exchanging binary data.
Notes: Image source: shutterstock_331435670

## Slide 13: Network Packets
13

## Slide 14: Packets
The binary data is grouped together into separate pieces, known as packets, and transmitted across the network .
Header | Sender’s IP address, receiver’s IP address, protocol | 96 bits
Payload | Data | 660 bits
Trailer | Indicates end of packet, error correction | 32 bits
The specific arrangement of packets allows the receiving party to properly interpret the contents and direction of the communication.
14

## Slide 15: Packets
For example, the version field is indicated in the header. As the first field, it starts at the first bit and ends at the fourth bit. The receiver will always find this information in this exact location.
01000101000000000000000111011010000001111000110001000000000000000100000000000110
In binary, 0100 translates to 4. This field indicates that this header uses Version 4.
15

## Slide 16: Protocol Example: Authentication
PAP (Password Authentication Protocol)
Username: Alice
Password: awesomeAlice1
Accept / Reject
Alice’s Personal Computer
Server
PAP Two-Way Handshake
16

## Slide 17: Protocol Example: Authentication
Client request contains bits in a specific order and length, per the standard and rules of the protocol.
1 Byte | 1 | 2 Bytes | 1 Byte | Variable | 1 Byte | Variable
Code: 1 | ID | Length | User name length | Username | Password Length | Password
17
Alice’s Personal Computer
Server
Username: Alice
Password: awesomeAlice1
Accept / Reject

## Slide 18: Protocol Example: Authentication
1 Byte | 1 | 2 Bytes | 1 Byte | Variable | 1 Byte | Variable
Code: 1 | ID | Length | User name length | Username | Password Length | Password
The server receiving the request will know where to look in the bitstream for content: the username and password.
18
Username: Alice
Password: awesomeAlice1
Accept / Reject
Alice’s Personal Computer
Server

## Slide 19: Interpreting Protocols from Raw Binary Data
Security professionals rely on web tools to convert binary data and determine the protocol being used.
011100000110000101110000001000000111001101100101011011100111010000101101011101010111001101100101011100100110111001100001011011010110010100100000010100000100000101010000010101010101001101000101010100100010000001110000011000010111001101110011011101110110111101110010011001000010000000110111
19
To find out which protocol is in use, convert the binary data to a readable string.
string-functions.com/
binary-string.aspx
Notes: Image source: shutterstock_523613047

## Slide 20: Activity: Interpreting Protocols In this activity, you will continue to play the role of a security analyst at Acme Corp. You must convert raw binary data into a readable format and determine which protocol is being used. 15 Minutes
20

## Slide 22: Ports
22

## Slide 23: Ports Real World Analogy
23
Bob wants to show a video presentation to Alice, a coworker who works across town. Bob will be presenting from Room 33, the video conference room in his office building.
Bob told Alice to meet him at his office, but only gave her the building address, 150 Main Street.
Because Bob didn't specify which room he'd be in, Alice will be able to find the office building, but not Bob or the video presentation.
Notes: Image source: shutterstock_126493766

## Slide 24: Ports Real World Analogy
24
In this analogy, the address of the office building, 150 Main Street, is the IP address.
The video conference room, Room 33, is the port.
Since we know that Room 33 is the video conference room, we know that any meeting in Room 33 will involve video conferencing, even if we're not explicitly told what to expect from the meeting.
Similarly, port numbers can be associated with a specific network function and protocol.
Notes: Image source: shutterstock_290042774

## Slide 25: If we know which port number is being used, we know what type of protocol it’s being used for.
25
Notes: Image source: shutterstock_1299397507

## Slide 26: Ports and Security
Ports are the access points for transmitting and receiving data.
Ports are like doors that can be opened, closed, or accessible only to certain individuals.
It’s important that IT professionals do not allow unauthorized access to these points of entry. Unauthorized access can potentially lead to a breach.
26
Notes: Image source: shutterstock_173113379

## Slide 27: Virtual Ports
Computers don’t have enough physical space for every protocol, so we use software to create virtual ports.
Every protocol is assigned a numerical virtual port number.
The corresponding port is the destination port. It’s where other machines send data to communicate with that protocol.
  For example: A machine sending an HTTP message to a web server sends traffic to the server’s port 80.
27
Notes: Image source: shutterstock_606184016

## Slide 28: Port Numbers
01
02
03
System Ports
Registered Ports
Dynamic Ports
There are 65,536 virtual ports, numbered from 0 to 65535.
These ports are divided into three ranges:
28

## Slide 29: Port Numbers
29
Range Title | Range Number | Also Known As | General Explanation | 
System Ports | Range 0–1023 | Well-known ports | Restricted: Only the operating system or administrators can bind services to these ports. E.g., HTTP typically runs on port 80. Normal users can't launch services on port 80, so we can trust that machines accepting connections to port 80 are using it to send and receive HTTP traffic. | 
Registered Ports | Range 1024–49151 | User ports | “Normal” users launching their own services will do so using ports in this range. | 
Dynamic Ports | Range 49152–65535 | Dynamic ports/private ports | When a machine sends data to another machine, it must open a port to send from. This is called a source port. Source ports are randomly chosen from the dynamic range whenever a machine sends a message. | 

## Slide 30: Common Ports
Port 80 | HTTP | Sending web traffic.
Port 443 | HTTPS | Sending encrypted web traffic.
Port 21 | FTP | Sending files.
Port 22 | SSH | Securely operating network services.
Port 25 | SMTP | Sending emails.
Port 53 | DNS | Translating domains into IP addresses.
30

## Slide 31: Source / Destination Ports
151.20.0.145
Port 80
188.4.4.72
Port 50158
The client (initiator) has a source port.
Source ports are randomly generated from the dynamic port range (49152 - 65536).
31
“I’d like cat.jpg please.”
“OK. Here’s the file you asked for.”
The server (receiver), has a destination port, depending on the protocol. Destination ports don't change, so we can associate a port with a certain protocol.
Notes: Cat Shutterstock ID: 1041783286

## Slide 32: Activity: Ports In this activity, you will continue to play the role of a security analyst at Acme Corp. You will find the source and destination port for several network requests and determine the protocol for each destination port. 15 Minutes
32

## Slide 34
34
Notes: Image source: AdobeStock_56885471

## Slide 35: OSI Layers
35

## Slide 36
36
When data travels
across a network, it goes
through multiple steps
and processes to reach
its destination.
Notes: Image source: AdobeStock_256668210

## Slide 37: OSI Layers
37
The process of sending an email starts with the following steps: |  | Certain protocols are responsible for handling specific steps of data transmission:
Convert the text of the user's email into a format the email application can understand. |  | The IMAP or POP3 converts the text of a user’s email into a format any email application can understand.
Add the destination address and destination port to this data. |  | The TCP adds information about destination ports to this data.
Convert this packet to a format that can be transmitted through physical wires. |  | The IP adds destination address information to the email data.
1.
2.
3.

## Slide 38: The Open Systems Interconnection (OSI) Model
The OSI model provides a framework for categorizing and conceptualizing the large number of ports and protocols.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
The OSI model is a seven layer framework that allows security analysts to understand how communication works on a network, by detailing the processes, devices, and protocols in place at each layer.
38

## Slide 39: OSI Model
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
Data Received
Data Transmitted
[Physical Link]
Data
Data
Data
Segments
Packets
Frames
Bits
39

## Slide 40: Layer 1: Physical
40
The Physical layer is responsible for transmission of binary data through a physical medium. It handles how data is physically encoded and decoded.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
Notes: Image source: Shutterstock_447377149 (router); shutterstock_74973190 (blue cable); (black cable)

## Slide 41: Layer 2: Data Link
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
41
The Data Link layer establishes links between nodes. It also ensures data gets to its final destination without corruption, thus protecting data integrity.
Notes: Image sources: Shutterstock_447377149 (router, left); Routers, right: AdobeStock_244465090 (top); shutterstock_264840719 (middle); shutterstock_291540545 (bottom); shutterstock_348430685 (icons)

## Slide 42: Layer 3: Network
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
42
The Network layer routes data through physical networks using an IP address, deciding which physical path the data will take, and ensuring it gets to the correct destination.

## Slide 43: Layer 4: Transport
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
43
The Transport layer is responsible for actually transmitting data across the network. It puts data onto the network, and assigns source and destination ports.
Internet

## Slide 44: Layer 5: Session
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
44
The Session layer manages connections between ports on computers and handles data flow.

## Slide 45: Layer 6: Presentation
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
45
The Presentation layer is is the translator for the network. It formats data to be presented to the Application layer, handles data representation, decryption and encryption, character set translation, and conversion.
Notes: Image source: shutterstock_281532896 (locks); shutterstock_749592787 (keys)

## Slide 46: Layer 7: Application
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
46
Website
The Application layer represents data so the consuming application understands it. This is the layer an individual interacts with, such as a web or email application.
Notes: Image sources: shutterstock_697523956

## Slide 47: Encapsulation: Data Traveling Through Layers
Data moves through the layers, starting from Layer 7 and ending at Layer 1, in a process known as encapsulation.
User data converted for transmission
Upper layer data
Upper layer data
Upper layer data
Upper layer data
TCP Header
TCP Header
TCP Header
FCS
IP Header
IP Header
LLC header
MAC header
111010101111101101001100101010 → Sent to cable
Network Media
Application
Presentation
Session
Transport
Network
Data Link
Physical
47
Encapsulation is the process of placing headers, and sometimes trailers, around the data to direct it to its destination.
Network Media

## Slide 48: Encapsulation Example
At the Transport layer, data is added to the TCP header based on the protocol being used.
At the Network layer, the destination IP address is added to the IP header to determine where the data is being sent outside of the local network.
At the Data Link layer, the destination MAC
address is added to the MAC header
in to determine what local machine to send the data to.
In summary, TCP, IP,
and MAC headers encapsulate the data.
These examples of encapsulation occur as data moves across layers:
Upper layer data
Upper layer data
Upper layer data
Upper layer data
TCP Header
TCP Header
TCP Header
FCS
IP Header
IP Header
LLC header
MAC header
111010101111101101001100101010 → Sent to cable
Network Media
Presentation
Session
Transport
Network
Data Link
Physical
48
User data converted for transmission
Application

## Slide 49: Decapsulation
Decapsulation is the process of removing the headers, and sometimes trailers, around the data to confirm the data reaches the destination.
49
Upper layer data
Upper layer data
Upper layer data
Upper layer data
TCP Header
TCP Header
TCP Header
FCS
IP Header
IP Header
LLC header
MAC header
111010101111101101001100101010 → Sent to cable
Network Media
Presentation
Session
Transport
Network
Data Link
Physical
User data converted for transmission
Application

## Slide 50: Decapsulation
At the Data Link layer, the receiving device analyzes the MAC header to see if it matches the recipient's MAC address, and moves to the next layer if so.
At the Network layer, the receiving device analyzes the IP header to see if it contains the right IP address.
If so, the header is removed and the data moves
to the next layer.
At the Transport layer, the TCP
header is analyzed
to determine the
destination port
for further processing the data.
In summary, TCP, IP, and MAC headers are decapsulated.
These examples of decapsulation occur as data moves across layers in reverse order:
User data converted for transmission
Upper layer data
Upper layer data
Upper layer data
Upper layer data
TCP Header
TCP Header
TCP Header
FCS
IP Header
IP Header
LLC header
MAC header
111010101111101101001100101010 → Sent to cable
Network Media
Presentation
Session
Transport
Network
Data Link
Physical
50
User data converted for transmission
Application

## Slide 51: OSI Model
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
Application 1
UserData
UserData
UserData
Data Frame
Additional data in the Frame added for security, addressing, etc.
UserData
UserData
UserData
Data Frame
Eg. Profibus, DeviceNet, Ethernet
Only the user data is presented to the application.
Network Cable
51
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
Application 2
Only the user data is presented to the application.
Notes: This graphic depicts the progression of data from one application to application. As it travels from the source application, it adds additional data to ensure it arrives at the correct destination securely. As it approved the source application, that additional data is removed, ensure that the application only receives the user data that was originally sent.

## Slide 52: OSI Model
An email moving through the OSI layers:
Layer 7: Application: The user types an email in Microsoft Outlook.
Layer 6: Presentation: The email text is converted from plain text into a version the receiving server can understand.
Layer 5: Session: A session with the receiving mail server is initiated.
Layer 4: Transport: Since email uses SMTP, it assigns the SMTP destination port and initiates a handshake with the mail server.
Layer 3: Network: The mail server destination IP is added.
Layer 2: Data Link: The MAC address of the router is added so the email can be sent outside of the local network.
Layer 1: Physical: The digital email is converted into a signal to be transmitted over a physical cable.
52

## Slide 53: OSI and Security
For example: If you find out that NetBIOS is a Layer 5 protocol, you immediately know that it's involved in managing user sessions, even if you've never heard of NetBIOS before.
For example: If you realize you're having a Layer 3 issue, you know you should start investigating your routers, even if you don't know exactly what the problem is.
For example: If you know a SQL injection attack is occurring, you can explain to your management that you need a Layer 7 web application firewall to identify and mitigate the attack.
53
The OSI model helps us more easily understand new protocols.
The OSI model helps determine where problems in the network are occurring, even if we don't have full knowledge of the issue.
The OSI model makes it easier to communicate where a security attack has occurred and what should be done.

## Slide 54: Activity: OSI Layers In this activity, you will continue to play the role Security Analysts at Acme Corp. You will be analyzing 10 suspicious network-related activities that have recently occurred at Acme Corp. Your task is to document at which OSI layer each of these situations occurred. 15 Minutes

## Slide 56: Wireshark
56

## Slide 57: Wireshark is a tool that allows us to look at real-time communication across a network and monitor the activities of connected devices.
57

## Slide 58: Packets and Wireshark
Communication between devices over a network is facilitated through the transfer of packets.
58

## Slide 59: Installing Wireshark
59

## Slide 60: 10 Minutes Activity: Wireshark Install In this activity, you will be installing the Wireshark desktop application which will be used several upcoming activities.

## Slide 61: Revisiting Packets
Networks communicate with sequences of binary data called packets. Wireshark is a packet capturing tool.
Application
Presentation
Session
Transport
Network
Data Link
Physical
Data
Data
Data
Segments
Packets
Frames
Bits
Each packet contains fields of information such as the address of its origin, the destination address, and the information that connects to the related packets being sent.
61
Communicating over a network is not entirely secure. These packets can be intercepted and analyzed by other users on the network.
Header | Sender’s IP address Receiver’s IP address Protocol | 96 bits
Payload | Data | 660 bits
Trailer | Indicates end of packet, error correction | 32 bits

## Slide 62: Packets and Wireshark
Wireshark does this analysis by inspecting individual packets.
Multiple packets collected into a file by Wireshark are called a packet capture. These have file extensions such as .cap, .pcap, and pcapng.
Wireshark is a tool that allows us to look at real-time communication across a network, and monitor the activities of the devices connected to it.
62
Notes: Logo is low risk

## Slide 63: Packets and Wireshark
In these packet captures, Wireshark collects and analyzes the kinds of websites and webpages individuals on the network are viewing, as well as the type of communication occurring.
63

## Slide 64: Wireshark Professional Context
Security professionals will often analyze network logs in order to research security-related issues.
For example:
Your manager has tasked you with analyzing web traffic to determine which source ports your system is using for HTTP requests. They want to make sure these aren't being blocked by your firewall.
You’ve been provided a capture of the logs they want you to analyze.
64
We’ll cover these scenarios in the next demo.
Notes: Image source: shutterstock_1240165258

## Slide 65: Wireshark
65

## Slide 66: Activity: Capturing Packets In this activity, you will continue to play the role of a security analyst at Acme Corp. You will configure your Wireshark application with the five requested configuration settings provided by your manager. 15 Minutes
66

## Slide 68: Analyzing HTTP Traffic Setup
In the next demonstration, we will analyze HTTP web traffic with the following scenario:
Your manager wants you to make sure a new employee, Michael, is in fact working hard on his first day of work.
You could ask Michael if you could view his browser history, but, he could have cleared his browser history, or used more than one browser.
Fortunately, the networking team has a packet capture of Michael's web traffic, and you can use Wireshark to easily analyze the following:
What websites has Michael visited?
Were any communications sent from these websites?

## Slide 69: Analyzing HTTP Web Traffic

## Slide 70: 15 Minutes Activity: Analyzing HTTP Data In this activity, you will analyze web traffic to determine if Sally Stealer is a spy for your rival company, WidgetCorp. You will also inspect the logs to see if Sally is sending any communications to WidgetCorp.

## Slide 72: Questions?